## Slide 1: Computational Foundations of Cyber Physical Systems (CS61063)
Strategies of Delay-Aware CPS Design

## Slide 2: The Problem
Consider two control tasks T1 and T2 are running on a single processor with periodicity p1= 0.4 and p2= 0.6. They are RM schedulable. Now an authentication task T3 is also introduced with periodicity p3 = 0.3 in order to secure the system against unauthorized access.
Task | Time for Control Task Execution (s) | Deadline (s) (same as their periodicities) | Priority
Control Task T1 | 0.15 | 0.4 | 2
Control Task T2 | 0.25 | 0.6 | 3
Security Task T3 | 0.05 | 0.3 | 1

## Slide 3: Observations
Notice that they are not RM schedulable anymore (why? we will discuss)
What are the strategies that can be useful in such case to schedule them?
Such strategies can be useful
  to handle delay in embedded controller implementations
  to handle packet drops in networked CPS

## Slide 4: Sensor to Actuator Delay Scenarios
Scenario 1 : Sensor to actuator delay < Deadline Strategy : Consider Delay while discretizing the continuous closed-loop system (Learnt earlier)
Control Task of interest
OtherTasks

## Slide 5: Sensor to Actuator Delay Scenarios
Scenario 2 : Sensor to actuator delay > Deadline
In every hyperperiod :
The same fixed-priority static RM schedule will be repeated
The control task will miss its deadline
This gives rise to a Deadline Hit/Miss Pattern (we will see)
Control Task of interest
OtherTasks
Delayed Execution

## Slide 6: Sensor to Actuator Delay Scenarios
Strategy :
Kill the Control Task that misses the deadline or
Strategically drop a control task to accommodate the current one
Strategy chosen depending on (i) control performance (ii) processor utilization
This gives rise to a Control Execution/Skip Pattern (We will see)
Control Task of interest
Other Tasks
Idle

## Slide 7: Scheduling with Deadline Hit/Miss Pattern
Problem: Not RM schedulable : 1st instance of T2 (T2,1) can miss its deadline.
Solution 1: (T2,1) should be dropped in every hyperperiod to accommodate others.
  We can see a Deadline Hit/Miss Pattern Here!
  Deadline Miss is denoted using 0 and Deadline Hit is denoted using 1
Deadline Hit/Miss Pattern for T1 : 1 1 1 [Arrives 3 times in a hyperperiod]
Deadline Hit/Miss Pattern for T2 : 0 1 [Arrives 2 times in a hyperperiod]
Deadline Hit/Miss Pattern for T3 : 1 1 1 1 [Arrives 4 times in a hyperperiod]

## Slide 8: Scheduling with Control Execution/Skip Pattern
Solution 2: (Considering the robustness of control) Execution of the 2nd instance of T1 (T1,2) can be skipped in every hyperperiod to accommodate others.
  We can see a Control Execution Pattern Here!
    Control Execution denoted using 1 and Control Execution Skip denoted using 0
Control Execution/Skip Pattern for T1 : 1 0 1 [Arrives 3 times in a hyperperiod]
Control Execution/Skip Pattern for T2 : 1 1 [Arrives 2 times in a hyperperiod]
Control Execution/Skip Pattern for T3 : 1 1 1 1 [Arrives 4 times in a hyperperiod]

## Slide 9: Scheduling with Control Execution/Skip Pattern
Control Execution/Skip Pattern for T1 : 0 11 [Arrives 3 times in a hyperperiod]
Control Execution/Skip Pattern for T2 : 1 1 [Arrives 2 times in a hyperperiod]
Control Execution/Skip Pattern for T3 : 1 1 1 1 [Arrives 4 times in a hyperperiod]
  [Control Execution denoted using 1 and Control Execution Skip denoted using 0]
Solution 3: (Considering the robustness of control) Execution of the 1st instance of T1 (T1,1) can be skipped in every hyperperiod to accommodate others.

## Slide 10: In a Nutshell
Among these 3 solutions we chose the one with
  Least Processor Utilization
  Least increment in control cost/ minimal worsening of control performance
  There are tool-chains available to analyze such delay-aware control strategies
  eg. Truetime, Jittertime etc.
  (We will see more on these in tutorial)