## Slide 1: Computational Foundations of Cyber Physical Systems (CS61063)
Soumyajit Dey
CSE, IIT Kharagpur
Physical Sys1
Physical Sys3
Physical Sys2
Controller
Controller
Controller
…............
Cyber World
APPLICATION OF CONTROL THEORY IN RT-SCHEDULING

## Slide 2
Control Theory
Control is a process of causing a system variable to follow some desired value called reference value.
A control system is one which can control any quantity of interest in a machine, mechanism or other equipment in order to achieve the desired performance or output.
Control Theory deals with the behavior of Dynamical Systems with inputs, and how their behavior is modified by feedbacks to maintain a desired performance.

## Slide 3
Application of Control theory in scheduling
Abdelzaher, Tarek F., John A. Stankovic, Chenyang Lu, Ronghua Zhang, and Ying Lu. "Feedback performance control in software services." IEEE Control Systems Magazine 23, no. 3 (2003): 74-90.
  ﻿Described the internal architecture of a typical Web server, present its dynamic model, and elaborate on the equivalents of sensors and actuators in this computing system.
  Discussed how the application of classical feedback control offers a solution to the problem of achieving performance guarantees for the software systems with an example of Web Servers.

## Slide 4
Web Service Architecture for a ﻿distributed client-server system in which succession of requests (many thousands of requests per second ) arrives at a server from clients across a communication network.
﻿For the server to yield acceptable performance, the order of request service times must be much smaller than the order of tolerable server response times.
Feedback performance control in software services

## Slide 5
A key prerequisite to system modeling is to define the actuators and their manipulated variables. Actuators in web server can be classified –
  Quality Adaption Actuators – Alters the processing requirements of the service request. It offers a flexible tradeoff between delay and quality.
  Resource Reallocation Actuators - Alters the amount of resources available for the processing of the request queue.
  Input Flow Actuators - Manipulates the input workload of a server and used when different clients have different priority.
Performance metrices can be–
  ﻿Queuing delays, execution latencies, and service response times.
  Connection bandwidth, service throughput, and packet rate.
  Derived metrics like the relative delay of two traffic classes, hit of a cache
Feedback performance control in software services

## Slide 6
Feedback performance control in software services
y(k) denotes the output or performance (e.g., delay or Queue throughput) reported at the kth sampling instant.
﻿u(k) denotes the control input at kth instant
﻿x(k) is the state vector
A, b and C describe the system model.
Service modeling

## Slide 7
Feedback performance control in software services

## Slide 8
Real-time Systems
A real-time system is any information processing system that has to respond to externally generated input stimuli within a finite and specified period.
The correctness depends on not only the logical result but also the time it is delivered.
Failure to respond is as bad as the wrong response.

## Slide 9
Application of Control theory in scheduling
Lu, Chenyang, John A. Stankovic, Sang H. Son, and Gang Tao. "Feedback control real-time scheduling: Framework, modeling, and algorithms." Real-Time Systems 23, no. 1 (2002): 85-126.
﻿ This paper presents a framework for adaptive real- time systems with following contributions-
  A scheduling architecture that maps the feedback control structure to adaptive resource scheduling in real-time systems
  A set of performance specifications and metrics to characterize both transient and steady state performance of adaptive real-time systems
  A control theory based design methodology for resource scheduling algorithms to satisfy system performance specifications.

## Slide 10
Feedback Control Real-Time Scheduling: Framework, Modeling, and Algorithms
Monitor (﻿measures the controlled variables )
Controller (﻿compares the performance references with corresponding controlled variables and computes a change called the control input based on the errors)
Qos Actuator (﻿dynamically changes the total estimated requested performance at each sampling instant k according to the control input by adjusting the QoS levels of tasks)
Basic Scheduler (﻿schedules admitted tasks with a scheduling policy e.g., EDF or Rate/Deadline Monotonic)
FCS (Feedback Control Scheduling)
architecture-
Notes: The Basic Scheduler schedules admitted tasks with a scheduling policy.
The Monitor measures the deadline miss ratio and CPU utilization at the kth sampling instant and feeds the samples back to the Controller.
The Controller compares the performance references with corresponding controlled variables to get the current errors.
The QoS Actuator dynamically changes the total estimated requested utilization according to the control input by adjusting the QoS levels of tasks.

## Slide 11: Task Model

## Slide 12
Feedback Control Real-Time Scheduling: Framework, Modeling, and Algorithms
Performance Specifications and Metrics:
Performance Profile:
                Stability, Transient-state response, Steady-state error, Sensitivity
Control related variables:
﻿Miss ratio M(k) at the kth sampling instant is defined as the number of deadline misses divided by the total number of completed and aborted tasks in a sampling window
﻿Utilization U(k) at the kth sampling instant is the percentage of CPU busy time in a sampling window

## Slide 13
Modeling Control system﻿
The control input to the controlled system is the change in the total estimated utilization DB(k). The output of the controlled system includes the controlled variables, miss ratio M(k) and utilization U(k).
﻿Derivation of model from the control input to the output-
Feedback Control Real-Time Scheduling: Framework, Modeling, and Algorithms
B(k) and B(k+1) are the ﻿total estimated utilization in the current and next sampling instant respectively and DB(k) is the control input at every sampling instant k
﻿Since the precise execution time of each task is unknown and time varying, the total (actual) requested utilization A(k) may differ from the total estimated requested utilization B(k). ﻿Ga(k), called the utilization ratio, is a time-variant variable that represents the extent of workload variation in terms of total requested utilization.
Since Ga(k) is time variant, we use the maximum possible value GA = max{Ga(k)}, called the worst-case utilization ratio

## Slide 14
Feedback Control Real-Time Scheduling: Framework, Modeling, and Algorithms
﻿The relationship between the total requested utilization A(k) and the controlled variables are nonlinear due to saturation, i.e., the controlled variables remain constant when the control input DB(k) ≠ 0.
When the CPU is underutilized (A(k) ≤ 1), the utilization U(k) is outside its saturation zone and equals A(k);
When the CPU is overloaded, however, U(k) saturates at 1 because it can never exceed 100%.
Based on previous equations, the analytical model for the utilization output is as following:

## Slide 15
Feedback Control Real-Time Scheduling: Framework, Modeling, and Algorithms
Derivation of the model for the miss ratio output M(k)
In contrast with U(k) that saturates in overload conditions, M(k) saturates at 0 when the CPU is underutilized, i.e., the total requested utilization is below a utilization threshold Ath(k) for the system’s particular workload in the kth sampling period.
When A(k) > Ath(k), M(k) usually increases nonlinearly with the total requested utilization A(k).Relationship between M(k) and A(k) needs to be linearized by taking the derivative at the vicinity of the performance reference MS as the miss ratio factor Gm. The miss ratio factor Gm can be estimated experimentally by plotting a miss ratio curve as a function of the total utilization based on experimental data.
﻿Given the miss ratio factor, we have the following linearized formula for the purpose of control design:
Where GM is the maximum slope at the vicinity of MS in control design to guarantee stability.
The analytical model for the miss ratio output:

## Slide 16
﻿Analytical model for the
miss ratio output-﻿
Analytical model for the
utilization output-
﻿Equivalent transfer functions
outside their own unsaturated zones
Feedback Control Real-Time Scheduling: Framework, Modeling, and Algorithms
Notes: (1-z^{-1})M(z) = G_MG_Az^{-1}D_B(z)\\
\frac{M(z)}{D_B(z)}=G_MG_A\frac{z^{-1}}{(1-z^{-1})}=G_MG_A\frac{1}{(z-1)}

## Slide 17
Models of Feedback Control Loops:
They have used use a simple P (Proportional) control function to compute the control input.
Feedback Control Real-Time Scheduling: Framework, Modeling, and Algorithms
Where,
DB(k) = Control Input
KP = a Tunable Parameter
E(k) = Error of the controlled variable

## Slide 18
Application of Control theory in scheduling
Mishra, Nikita, Connor Imes, John D. Lafferty, and Henry Hoffmann. "Caloree: Learning control for predictable latency and low energy." ACM SIGPLAN Notices 53, no. 2 (2018): 184-198.
﻿ This paper presents a control theory based resource manager that learns key control parameters to meet latency requirements with minimal energy at runtime for dynamic system.
  A scheduling architecture that maps the feedback control structure to adaptive resource scheduling in real-time systems
  A set of performance specifications and metrics to characterize both transient and steady state performance of adaptive real-time systems
  A controller for resource scheduling algorithms to satisfy system performance specifications.
  ﻿A learner to customize control systems at runtime, ensuring application latency both formally and empirically with no prior knowledge of the controlled application

## Slide 19
CALOREE: Learning Control for Predictable Latency and Low Energy
The controller sends the learner a new application’s name and device type.
The learner determines how many samples are needed for an accurate prediction.
The controller takes these samples and sends the latency and power of each measured configuration to the learner.
The learner predicts the optimal configurations which uses the learned model from then on.
Workflow between Learner and Controller

## Slide 20
CALOREE: Learning Control for Predictable Latency and Low Energy
﻿Temporal relationship of learning and control

## Slide 21
Traditional control for computing
Where,
  ﻿x ﻿∈ ℝq is is the controller’s state, capturing the relationship between resources and goals; q is the controller’s degree, or complexity of its internal state
  u(t) ∈ ℝn represents the current resource configuration; i.e., the ith vector element is the amount of resource i allocated at time t.
  y(t) ∈ ℝm represents the value of the goal dimensions at time t.
  The matrices A ∈ ℝqxq and B ∈ ℝqxn relate the resource configuration to the controller state. The matrix C ∈ ℝmxq relates the controller state to the expected behavior.
This control definition does not assume the states or the resources are independent, but it does assume a linear relationship.
CALOREE: Learning Control for Predictable Latency and Low Energy
Eq. 1

## Slide 22
Drawbacks of traditional control:
  ﻿requires matrix computation, and has high overhead
  ﻿adaptive mechanisms are not parameter-free
  need prior knowledge of ﻿user-specified parameters
CALOREE transforms a standard control system into one that works without prior knowledge of ﻿user-specified parameters by -
  ﻿controlling speedup (an abstraction on performance) rather than resources
  ﻿translating speedup into an energy minimal resource schedule in a separate step
  ﻿exploiting the problem structure to solve scheduling problem in constant time
  ﻿These steps assume a separate learner has produced predictions of how resource usage affects latency and power.
CALOREE: Learning Control for Predictable Latency and Low Energy

## Slide 23
CALOREE: Learning Control for Predictable Latency and Low Energy
CALOREE’s control law
﻿﻿Using these substitutions, x is eliminated from Eq. 1 to relate speedup to latency by,
﻿CALOREE converts traditional control Equation Eq.1 into a single-input (latency), single-output (speedup) controlling using A = 0, B = b(t), C = 1, u = speedup, and y = perf(t); where b(t) is a time-varying parameter representing the application’s base speed (the speed when all resources are available)and perf is the measured latency.
CALOREE targets to eliminate the error between the goal and calculated performance-

## Slide 24
CALOREE: Learning Control for Predictable Latency and Low Energy
﻿CALOREE uses this control equation
﻿which states that the speedup at time t is a function of the previous speedup, the error at time t, the base speed b(t), and the controller’s pole, ρ(t).
Standard control techniques statically determine the pole and the base speed, but CALOREE dynamically sets the pole and base speed to account for error in the learner’s predictions.
For stable control, CALOREE ensures 0 ≤ ρ(t) < 1
﻿Small values of ρ(t) eliminate error quickly, but make the controller more sensitive to the learner’s inaccuracies whereas larger ρ(t) makes the system more robust at the cost of increased convergence time.
Controlling speedup

## Slide 25
Maity, Srijeeta, Anirban Ghose, Soumyajit Dey, and Swarnendu Biswas. "Thermal-aware Adaptive Platform Management for Heterogeneous Embedded Systems." ACM Transactions on Embedded Computing Systems (TECS) 20, no. 5s (2021): 1-28.
﻿ This paper presents a framework for adaptive dynamic thermal management for real- time systems with following contributions-
  Performs online thermal management of heterogeneous CPU-GPU platforms executing multiple real-time tasks that supports dynamic changes in the job set that can result in dynamic thermal violations
  Provides an OpenCL run-time platform manager which adaptively handles dynamic thermal violations by formulating lightweight heuristic-guided scheduling solutions
  Considered a combination of runtime task partitioning, migration, idleness insertion, and control theoretic DVFS as scheduling moves for CPU-GPU heterogeneous systems.

## Slide 26
Context: Car with ADAS approaching congested area from highway
Requirement: Increase rate of Pedestrian detection?
Dynamic change in job set
Dynamic Scheduling
Real-time constraint
Thermal constraint
Need for adaptive, lightweight, thermal aware resource manager
A-DTM
Proposed framework
Thermal-aware Adaptive Platform Management for Heterogeneous Embedded Systems
Designing an efficient thermal-aware, adaptive resource manager, that is cognizant of the application performance, as well as the thermal profile, is a challenging problem for heterogeneous multi-cores.
Prior work does not address the issue of real-time task scheduling in CPU-GPU integrated systems while handling thermal violations in case of dynamic workload modifications

## Slide 27
OpenCL (Open Computing Language) is a framework for writing programs that execute across heterogeneous platforms. It provides a standard interface for parallel computing using task and data level parallelism on different compute devices such as CPU, GPU, FPGA and DSP.
Partitioning tasks in the context of OpenCL applications entail splitting the data space to be processed by the task/kernel into segments and processing the segments concurrently or sequentially using the devices of the heterogeneous system.
Thermal-aware Adaptive Platform Management for Heterogeneous Embedded Systems
CPU
GPU
DSP
FPGA
Y% to GPU
X% to CPU
CPU
K1
GPU
CPU
GPU
time

## Slide 28
Thermal-aware Adaptive Platform Management for Heterogeneous Embedded Systems
𝜏
𝜏i
Profile tasks
Choose suitable task partitioning size
Profile partitioned sub-task
Offline phase
Recovery controller
Thermally stable schedule
Initial
task mapping
Online phase
Updated task mapping
Dispatch sub-tasks
Task schedule
Monitor thermal violation
WCET lookup table
Methodology overview
𝒥'
For faster thermal recovery actions by modifying task mapping choices , the granularity of task mapping is reduced from tasks to sub-tasks level.
In the offline phase, the tasks are profiled extensively and suitable task partitioning size is computed and again profiled for getting the WCET for each sub task.
In the online phase, the subtasks are dispatched following an initial task schedule and the thermal behaviors are monitored . In case of thermal violations, a recovery controller gets triggered in the framework that modifies the task schedule adaptively.

## Slide 29
Local recovery
Global recovery
No violation
Dispatch 𝜏k
Recovery
controller
𝐓 > 𝐓major
𝐓major> 𝐓 > 𝐓minor
𝐓 < 𝐓minor
Schedule 𝑆
Odroid XU-4
Updated mapping for next sub-task
in the same hyper-period
Peak temperature
(𝐓)
𝜏k’
< 𝜏k , ... >
𝒎’k’
< 𝒎’k , ... >
Updated schedule for next hyper-period
No
update
Thermal-aware Adaptive Platform Management for Heterogeneous Embedded Systems
Recovery controller workflow
They have considered two thermal thresholds- TMajor and Tminor
If peak temperature, during a task execution lies between Tmajor and Tminor local recovery is activated which makes some local changes in the task mapping of the immediate next sub to reduce the temperature.
If peak temperature goes beyond Tmajor Global recovery is activated to avoid default thermal throttling. Global recovery identifies the tasks responsible for major violation, and changes the task mapping of the concerned tasks for the next hyper-period and this continues until major violation is mitigated.

## Slide 30
Nth
Hyper-period
Minor Violation
Local Controller
Local Controller
Minor Violation
Sub-task of τ1
Sub-task of τ2
Sub-task of τ3
CPU
GPU
interval
Nth hyper-period
Major Violation
Sub-task of τ1
Sub-task of τ2
Sub-task of τ3
CPU
GPU
...
GlobalController
GPU
CPU
...
N+rth hyper-period
Thermal-aware Adaptive Platform Management for Heterogeneous Embedded Systems
Local recovery
Global recovery
Frequency tuning
Task migration
Frequency tuning
Task migration
Examples of local and global recovery

## Slide 31
Designed a controller routine that takes control theoretic scheduling decisions to choose appropriate recovery actions to be applied for the next hyper-period based on the observed values of device utilization and frequency settings in current hyper-period.
Each device in the platform can have a total of 22possible configurations of device utilization and frequency settings. There are two devices (CPU and GPU), they examine 22x2 = 16 different scenarios
Table 1 summarises the recovery actions taken by the controller for each of the sixteen different scenarios
Thermal-aware Adaptive Platform Management for Heterogeneous Embedded Systems
Control action selections

## Slide 32
Thermal-aware Adaptive Platform Management for Heterogeneous Embedded Systems

## Slide 33
Thank you!